| 023-4350-0 | TG-3: Temperature Display |
| --- | --- |

TEMPERATURE DISPLAY

A Kussmaul TG-3 Series Model #023-4350-0 digital temperature display shall be installed.  The display shall have the following:

1.  Sensor range: -20 to 160 degree F (-29 to 71 degrees Celsius)

2.  Three zone input

3.  LCD read out accurate with 1% + / - degree with full scale

4.  Five level back lighting “ON” LED display

5.  Programmable high/low temperature alarm, activates 85 db warning buzzer

6.  Waterproof face and 2.125” mounting hole

7.   Programming via instrument front buttons

8.   One remote temperature sensor with 20 feet of cable