| 091-11-12 | Auto Charge 11 |
| --- | --- |

DUAL BATTERY CHARGER

A Kussmaul Auto Charge 11 Series Model #091-11-12, 10 amp dual battery charger shall be installed.   The charger shall include a front panel amp meter shall indicate output current with protective front panel and strain relief.     The charger shall be UL listed.

The charger shall have the following operational specifications:

a)  120 volts AC input at 2.5 amps

b)  12 volts DC output at 10 amps

c)   Dimensions of:  11.375” high x 5.5” wide x 4.375” deep and weighs 12 lbs.

The battery charger shall supply a ‘dual battery banks’ utilizing independent sense circuits that control voltage and current to each battery, so that parasitic loads on one battery have no effect on the second battery bank.    The unit shall be enclosed in an aluminum enclosure.   The system shall have a built-in sense circuit to check battery voltage 120 times a second.

Full amperage output shall be available to either battery if the adjacent bank does not require charging, optimizing use of available power then charging banks with differing parasitic loads.  The unit shall include front panel connections for a remote display.