| 091-118-12 | Euro Charger III, 12 Volt |
| --- | --- |

BATTERY CHARGER

A Kussmaul Euro Charger III Series Model #091-118-12, 18 amp high output battery charger shall be installed.    The charger shall include a front panel mounted amp meter that indicates total output current and protective panel with strain relief connections.   The unit shall meet CE requirements.

The charger shall have the following operational specifications:

a)  120/240 volts AC input at 4.7/2.4 amps

b)  12 volts DC output at 18 amps

c)   Dimensions of:  12.75” high x 6.75” wide x 4.25” deep and weighs 19 lbs.

The battery charger shall supply ‘triple battery banks’ utilizing independent sense circuits that control voltage and current to each battery, so that parasitic loads on one battery have no effect on the other battery banks.   The unit shall be enclosed in an aluminum enclosure.   The system shall have a built-in sense circuit to check battery voltage 120 times a second.

Full amperage output shall be available to either battery if the adjacent bank does not require charging, optimizing use of available power then charging banks with differing parasitic loads.  The unit shall include front panel connections for a remote display.