| 091-12HO-PIM | Auto Charge 12 HO-PIM |
| --- | --- |

BATTERY CHARGER

A Kussmaul Auto Charge #12 Series Model #091-12HO-PIM, 20 amp high output battery charger shall be installed.   The charger shall include a front panel amp meter to indicate output.

The unit shall include a 120 volt AC outlet in the front panel, with two (2) 15 amp GFI duplex outlets, with circuit breaker protection for plug in of accessory 120 volt equipment.

The charger shall have the following operational specifications:

a)  120 volts AC input at 4.7 amps

b)  12 volts DC output at 20 amps

c)  Dimensions of:  12.75” high x 6.75” wide x 4.25” deep and weighs 19 lbs.

The battery charger shall supply a ‘single battery bank’ with automatic operation and with an aluminum enclosure.