| 091-170-DV-24 | Auto Charge 12 HO-DV, 24V |
| --- | --- |

BATTERY CHARGER

A Kussmaul Auto Charge #12 Series Model #091-170-DV-24, 12 amp dual voltage battery charger shall be installed.   The charger shall include a front panel amp meter to indicate output and protective front panel and strain relief.

The charger shall have the following operational specifications:

a)  Dual voltage:  120 volts AC input at 4.7 amps or 240 volts AC input at 2.3 amps

b)  24 volts DC output at 12 amps

c)   Dimensions of:  12.75” high x 6.75” wide x 4.25” deep and weighs 19 lbs.

The battery charger shall supply a ‘single battery bank’ with automatic operation and with an aluminum enclosure.   The unit shall include front panel connections for an optional remote display.