| 091-182-230-24 | Super 16 Auto Eject, 16A, 240V, 24V |
| --- | --- |

EJECTION UNIT

A Kussmaul Super 16 Auto Eject Euro Style Model #091-182-230-24, 16 amp 240 volt pin and sleeve contact shore power assembly, cover, solenoid input wire and plug shall be installed.   The 24 volt unit shall eject the shore power cord away from vehicle path upon sensing engine start; after ejection, the weatherproof cover snaps into position over inlet.  The unit shall have a waterproof sculpted cover with no sharp edges and back enclosure with watertight cable fittings, which protect mechanism from road contamination.   The unit shall sequence energizing of the Auto Eject, eliminating terminal arching when connecting and disconnecting power cord.   The unit shall have an IEC #60309 standard connector provided.

A pre-wired 3 foot solenoid input wire (side wired) shall be installed.   The assembly shall have the following dimensions: 5.6” high x 4.4” wide x 5.6” deep with 5 lb. weight.   Color of cover shall be:  (yellow) (red) (blue) (white) (gray) (black)