| 091-195-12-USB | Low Ripple Battery Saver HO, w/USB Port, 20A |
| --- | --- |

BATTERY SAVER

A Kussmaul Model #091-195-12-USB, Low Ripple series high output 20 amp Battery Saver with USB Port shall be installed.   A “power on” indicator shall be installed on the front panel.

The Battery Saver shall have the following operational specifications:

a)  120 volts AC input at 4.5 amps

b)  12 volts DC output at 20 amps

c)  USB output 5.0 volts, 1 amp

d)  Dimensions of:  11.75” high x 5.75” wide x 2.5” deep and weight 5 lbs.

The unit shall have a “fast acting” anti-glitch relay to remove auxiliary loads from the vehicle’s battery system and connect the load to the Battery Saver; which will prevent battery discharge when the vehicle is not in use.   The system shall have “clean low ripple output” which will not interfere with sensitive electronics.   The unit shall have a current limiter to prevent overload.   The Battery Saver shall be enclosed in an aluminum enclosure.