| 091-207-12-194B | LPC 20, w/Status Center |
| --- | --- |

BATTERY CHARGER AND STATUS CENTER DISPLAY

A Kussmaul Auto Charge LPC 20 Series Model #091-207-12-194B, Low Profile 20 amp battery charger shall be installed.   The charger shall include a Model #091-194B-IND “Status Center” exterior digital display.

The charger shall have the following operational specifications:

a)  120 volts AC input at 7 amps

b)  12 volts DC output at 20 amps

c)  Dimensions of:  3.3” high x 6.8” wide x 13.25” deep and weighs 7 lbs.

The lightweight and low profile battery charger shall supply a ‘single battery system’ and with an aluminum enclosure.   The unit shall include an auxiliary 15 amp output circuit with power source selector for operating accessory loads.   The unit shall include front panel connections for a remote display.   Charger output shall pose no interference with other electronic systems on the vehicle.