| 091-28 | Air Eject |
| --- | --- |

AIR EJECTION UNIT

A Kussmaul Air Auto Eject Model #091-28 air hose eject assembly, mating connector, and check valve, shall be installed.   The 12 volt 140 PSI unit shall eject the air hose away from vehicle path upon sensing engine start.  The vehicle side mounted pneumatic connector shall be suitable for standard air hose adapters to maintain air pressure on the vehicle’s air brake system in the unit is parked in a building.   (A minimum of 20 PSI shall be required for ejection operation.)

The assembly shall have the following dimensions: 3.6” high x 2.85” deep with 2 lb. weight.