| 091-55-20-120-BW | Super 20 Auto Eject, Back Wire, 20A, 120V |
| --- | --- |

EJECTION UNIT – BACK WIRED

A Kussmaul Super Auto Eject Model #091-55-20-120-BW, 20 amp 120 volt shore power assembly, cover, solenoid input wire, power cord, and plug shall be installed.   The 12 volt solenoid shall eject the shore power cord away from vehicle path upon sensing engine start; after ejection, the weatherproof cover snaps into position over inlet. The unit shall sequence energizing of an Auto Eject, eliminating terminal arching when connecting and disconnecting power cord.

The unit shall have a waterproof back enclosure with watertight cable fittings, which protect mechanism from road contamination.  A pre-wired 3 foot AC electrical cord and starting sense wire (back wired) shall be installed.

The assembly shall have the following dimensions: 6.17” high x 4.08” wide x 2.8” deep with 4 lb. weight.   Color of cover shall be:  (yellow) (red) (blue) (white) (gray) (black)