| 091-56-12-IND | Auto Charge 1000, w/Bar Graph Display |
| --- | --- |

BATTERY CHARGER, BUILT-IN BATTERY SAVER AND BAR GRAPH DISPLAY

A Kussmaul Auto Charge #1000 Series Model #091-56-12-IND, 15 amp battery charger and 3 amp Battery Saver shall be installed.    The charger shall include a Model #091-199-001 remote digital display.

The Battery Saver component shall eliminate drain on vehicle’s battery system when in vehicle is not in use.  The system shall automatically disconnect auxiliary vehicle loads from battery when the charger is energized.

The charger shall have the following operational specifications:

a)  120 volts AC input at 3.5 amps

b)  12 volts DC output at 15 amps

c)   Battery Saver:   3 amps 12 volt DC output

d)  AC power applied light on front panel

e)  Battery Saver circuit overloaded

f)  Dimensions of:  9.35” high x 5.9” wide x 4.725” deep and weighs 17 lbs.

The battery charger shall supply a ‘single battery bank’ with automatic operation and with an aluminum enclosure.   The system shall have a built-in sense circuit to check battery voltage 120 times a second; the system shall compensate for voltage drop in charging wires and provide quick recharging with no over-charging.  The unit shall include front panel connections for a remote display.