| 091-9-12V-AD | Auto Pump 12V, with Auto Drain |
| --- | --- |

AIR COMPRESSOR

A Kussmaul air compressor Model #091-9-12V-AD shall be installed.   The vehicle mounted air compressor shall ensure that the air brake system is properly pressurized for immediate response of the unit.   A pressure switch shall regulate operation and shall automatically sense low air pressure in the brake system and restore the proper pressure.

The unit shall have no interference with the vehicle mounted air compressor.   The compact compressor shall have sealed bearings and a 15 amp circuit breaker installed in pressure switch assembly.

The Auto Drain shall be installed on the outlet side of the air compressor and shall automatically purge water from the air discharge output.   The water shall be ejected from the water separator bowl every time the compressor cycles off via a 12 volt solenoid.

The air compressor shall have the following ratings:

1)  100 PSI maximum rating

2)  Pre-set at 75 PSI “ON” and 95 PSI “OFF”

3)  Adjustable differential range of 20 PSI to 100 PSI

4)  Output:

0.30 SCFM @ 80 PSI

0.35 SCFM @ 60 PSI

5)  Rating: 12 volt at 11 amps

6)  Dimensions of:   6.2” high x 4.30” wide x 14” deep and weighs 6 lbs.