| 091-9-12V | Auto Pump 12V |
| --- | --- |

AIR COMPRESSOR – 12 VOLT

The Auto Pump 12 volt driven air compressor shall ensure that the air brake system is properly pressurized for immediate response of the unit.   A pressure switch shall regulate operation and shall automatically sense low air pressure in the brake system and restore the proper pressure.   The unit shall have no interference with the vehicle mounted air compressor. The compact compressor shall have sealed bearings and a 15 amp circuit breaker installed in pressure switch assembly.

The air compressor shall have the following ratings:

1)  100 PSI maximum rating

2)  Pre-set at 75 PSI “ON” and 95 PSI “OFF”

3)  Adjustable differential range of 20 PSI to 100 PSI

4)  Output:

0.30 SCFM @ 80 PSI

0.35 SCFM @ 60 PSI

5)  Rating:   12 volt at 11 amps