| 445-5262-0 | EV-40, Charger |
| --- | --- |

BATTERY CHARGER

A Kussmaul #EV Series Model #445-5262-0 Low Profile 40 amp battery charger shall be installed.   The unit shall have 3-step charging, with lower float voltage maintenance mode for no overcharging.   Battery type selector switch for program use with Gel cell, flooded lead acid, or  AGM batteries.

The charger shall have the following operational specifications:

a)  90 to 250 volts AC auto range input at 6.2 amps

b)  12 volts DC output at 40 amps

c)  Dimensions of:  3.13” high x 6.8” wide x 13.12” deep and weighs 7 lbs.

The lightweight and low profile battery charger shall supply a ‘single battery system’ and with a red powder coat aluminum enclosure.   The unit shall include an auxiliary 15 amp output circuit with power source selector for operating accessory loads.   The unit shall include front panel connections for a remote display and auxiliary loads.   Charger output shall pose no interference with other electronic systems on the vehicle.