| 445-5393-0 | EV-20, Charger |
| --- | --- |

BATTERY CHARGER

A Kussmaul #EV Series Model #445-5393-0, Low Profile 20 amp battery charger shall be installed.   The unit shall have 2-step charging, with bulk-float, and no overcharging feature.

The charger shall have the following operational specifications:

a)  120/240 volts AC input at 3.1 amps

b)  12 volts DC output at 20 amps

c)   Dimensions of:  2.32” high x 6.8” wide x 13.12” deep and weighs 5 lbs.

The lightweight and low profile battery charger shall supply a ‘single battery system’ and with a red powder coat aluminum enclosure.   The unit shall include an auxiliary 15 amp output circuit with power source selector for operating accessory loads.   The unit shall include front panel connections for a remote display and auxiliary loads.   Charger output shall pose no interference with other electronic systems on the vehicle.