| 497-0400-5 | Digital Battery Analyzer, DBA |
| --- | --- |

DIGITAL BATTERY ANALYZER

A Kussmaul DBA Series Model #497-0400-5 digital battery analyzer shall be provided.  The unit shall be suitable for 6 or 12 volt DC, lead-acid (flooded, gel, or AGM) deep cycle or gen/engine start battery with a capacity of 100 to 1400 CCA.

The unit shall have the following features:

1)  Operating range:   5.5 to 14 volts DC

2)  Input power:   operates on power of battery under test, down to 5.5 volts DC

3)  Display:  LCD

4)  Temperature range:   32 to 120 degrees F (0 to 50 degrees Celsius) compensation provided below 32 degrees F

5)  Reverse polarity protection

6)  Acid resistant ABS plastic case

7)  Dimensions of 9” x 4” x 2.5” with .9lbs (.4kg)